## Slide 1: Precision regulation of radio frequency fields at FLASH
Christian Schmidt
for the LLRF & LbSyn team
LLRF workshop 2011
18.10.2011

## Slide 2: Outline
Motivation
  Innovations at FLASH
LLRF system
  System modeling
  Measurement results
  Controller cascading concept
First results from uTCA upgrade
  Achieved field stability
  Beam based measurements
Summary

## Slide 3: Motivation
Goal: Stable acceleration field seen by electron bunches
  Pulse to pulse
  Within macro-pulses
Disturbance suppression in the system
  Drifts, noise, temperature variation, vibrations
  Cavity detuning (vibration and deformation)
  Beam itself is disturbance from fields point of view
  Suppression of further modes in the system
Operability and reliability
  Recovering states after failures / trips
  Set-point = actual measurement point (not field value)
  Automation (2 control value for the operator)
Strategy for cascaded regulation concept

## Slide 4: Innovations since upgrade in 2010
Renovation LLRF system in injector area (GUN, ACC1, ACC39)
Equal hardware, firmware and software for all RF stations
Finite State Machine (start, stop, recover, ramping, …)
Learning Feed-Forward permanently running
Model-based complex feedback controller
Various correction tables, algorithms limiters (optimization and robustness)
Piezo actuators for detuning regulation
Charge scaled beam loading compensation
Beam-based feedbacks on different timescales
….

## Slide 5: Schematic view of LLRF Systems for FLASH
BLC
Toroid
BBF
Toroid
BAM
BCM
MIMO FB Controller
To design controller components, it is essential to understand (model) system behavior

## Slide 6: Identification of system dynamics
Courtesy S. Pfeiffer
White box model
Black box identification
Grey box Model
Cavity resonant circuit model
Black box model, additional system characteristics, no physics
Grey box models allow to combine both methods
  Specific excitation signals
  Fixed model structure
  Get physical insight

## Slide 7: Identification steps to validation
2 step identification for different frequency ranges
Model validation
Identification algorithm
Reliable procedure to determine system
Open loop model MIMO controller design
Closed loop model Learning FF

## Slide 8: Learning Feed-forward (LFF)
LFF off
LFF on
Phase [deg]
Voltage [MV]
1st bunch
Running for all RF stations incl. GUN
Reproducible set-points
Minimization of residual control errors
Minimization of energy-variation
Essential for RF regulation!
Algorithm baseline

## Slide 9: ACC1 control performance with 4.5 mA beam current
All field control applications are turned on:
LFF, MIMO FB, BLC
1st bunch start
dA / A ~ 9e-5 rms (intra pulse)
~ 7e-5 rms (pulse to pulse)
dP ~ 0.01 deg (both)
LFF stop

## Slide 10: Achieved energy stability during ILC tests (Feb 2011)
1200 bunches
~ 500 kV @ 1GeV

## Slide 11: Cascaded regulation concept
Intra-pulse RF regulation (1Mhz)
Pulse to pulse adaptation (10 Hz)
Feedback controller
Beam based feedback
Beam loading compensation
Cavity max gradient limiters
Table limitations
Learning Feed-forward
Beam based set-point corrections
Slow adaptation ( >1 Hz)
Loop gain and phase correction
Piezo resonance control
DAC offset compensation
Beam based set-point adaptation
Phase filling optimization
Keep in range

## Slide 12: Upgrade to uTCA standard
Standard | VME | uTCA
ADC | 14 bit | 16 bit
DAC | 14 bit | 16 bit
fs | 1 MHz | 9 MHz
N | 2048 | 16384
… |  | 
Thanks: F.Ludwig
Tunnel installation (XFEL)
Drift compensation
Scalability
Non-IQ sampling
…

## Slide 13: Excitation of the 8/9-Pi mode
Individual cavity
resonance frequencies
Filtering with controller
New modeling methods
Spread of cavities

## Slide 14: Amplitude stability as function of controller delay
8/9-pi mode
8/9-pi mode
stable area
stable area

## Slide 15: Measurements of beam induced transients
Possible advancement of vector sum calibration in terms of accuracy and machine
setup requirements (currently 3nC with 30 bunches)

## Slide 16: Measured amplitude and phase stability
uTCA System in control loop, with LFF and MIMO-Feedback
Higher bandwidth compared to VME, In-loop measurements fulfill XFEL specifications
Oscillations after filling
transition
Pulse to pulse variation
Preliminary data

## Slide 17: Amplitude pulse to pulse variation
Difference between out of loop measurement and beam based data probably due to link to optical synchronization system
Approx. 30 %
improvement
Preliminary data

## Slide 18: Arrival time variation
On-crest setup
1 bunch (high frequent oscillations)
Differential measurement BAM 3DBC2 – 1UBC2
Off-crest (SASE conditions)
30 bunches averaged ( f < 30 kHz)
Absolute meas. BAM 3DBC2
Preliminary data
Correlated errors from optical synchronization system are subtracted
Imperfections between optical synchr. and
RF are not excluded

## Slide 19: Summary
LLRF system in a reliable situation for machine operation
  Permanent developments and updates
  Reliable and reproducible set-points and stabilities
  Unification of the systems
Upgrade to uTCA Standard
  Hardware development in first iteration stage
  First measurement results at FLASH successful
  Planned full upgrade to FLASH as test bed for XFEL
Thanks for your attention

## Slide 20: Backup slides

## Slide 21: LLRF status server observes control performance
27th July, All RF stations show correlated regulation performance degradation
Also visible in beam based monitors

## Slide 22: Comparison 8/9-Pi mode excited and suppressed
~ 800 kHz oscillations
Controller settings are more critical due to higher sampling rate, filtering, averaging

## Slide 23: Identified uTCA model

## Slide 24: Identification response

## Slide 25: Notch filter structure in MIMO FB

## Slide 26: Measurement VME system with uTCA regulation
dA / A ~ 0.001 % , dP ~ 0.002 deg

## Slide 27: uTCA regulation performance
Measured with synchrotron radiation camera dE ~ 0.005 %

## Slide 28: Installation in Injector hutch, parallel to ACC1 (VME)

## Slide 29: Regelung von ACC39 bei gleichen Bedingungen
Höhere Bandbreite dieses Systems
größeren Störungen
Kompensation kann nur auf 1us genau eingestellt werden
Abtastfrequenz zu gering
Bereich des Bunchzugs
Timing zwischen LFF und der Beamloading Kompensation nicht optimal
Effekt ist im SASE Profil zu sehen

## Slide 30: LLRF station regulation overview

## Slide 31: LLRF station regulation overview